## Slide 1: IPM FOR Maintenance staff
Lesson 1 of 1
In-Person Education Module

## Slide 2: Learning Objectives
Explain the importance of routine, proactive building and facilities maintenance to maintain structural integrity and prevent pest entry and pest conducive conditions
Explain the importance of timely work order follow-up

## Slide 3: Learning Objectives
Describe the key elements of sanitation (clean environment) and exclusion, (habitat prevention) including: strategies, tactics, and tools
Describe the key elements of inspection and monitoring, including what to look for, where to look, tools used, and frequency
Explain the importance of effective communication, education, and cooperation between school staff

## Slide 4
What is IPM?
IPM = Integrated (Intelligent) Pest Management
A sensible, environmentally friendly, and effective way to solve pest problems

## Slide 5
Maintenance Staff and IPM
Maintenance responsibilities
Emergency responses daily
Landscaping and grounds

## Slide 6
Maintenance Staff and IPM
Maintenance staff are among the most important people in a school IPM program
  staff members regularly see every part of the school
  perform tasks to maintain a healthy learning environment
  maintain the school to help keep pests out and reduce pest and pest management associated risks
Why be involved in school IPM?

## Slide 7
Schools are great places for certain pests
Some find everything they need to survive
  Food
  Water
  Shelter
Pests Love To Go To School!

## Slide 8
Pests in schools
Awareness of common pests
Problematic pests in schools:
  Animal pests
  Plant pests

## Slide 9: 1.
IPM is Not an Additional Item on Your to-do List
Maintenance is a demanding job
IPM does not add to your responsibilities!
IPM
IPM is everyone’s job
Maintenance staff with young helper, moving debris from fallen tree - Jason Moore, Street Superintendent, City of Beatrice, Nebraska

## Slide 10
Maintenance Staff and IPM
Maintenance staff actually implement IPM as they go about their regular daily duties
Maintenance staff installing a rain gutter on a building - Ethoseo from Wikimedia commons

## Slide 11
Maintenance Staff and IPM
Routine, proactive maintenance
  Maintain structural integrity
  Prevent pest entry and pest conducive conditions
Gaps in foundation provide access to pests such as rodents - Dawn H. Gouge, University of Arizona

## Slide 12
Routine, Proactive Maintenance
Structural integrity
Regular monitoring of buildings
Perform structural repairs as soon as possible
Maintain structural integrity of buildings
Gaps in wall plaster can lead to moisture retention and weakening

## Slide 13
Routine, Proactive Maintenance
Moisture management
Avoid moisture accumulation in and around the buildings
Waterproofing using quality materials
Maintain structural integrity of buildings
Avoid water accumulation around building foundation – Shaku Nair, University of Arizona

## Slide 14
Routine, Proactive Maintenance
Incorrect placement of splash-guards (left) leads to puddling of water near building foundation and soil erosion – Shaku Nair, University of Arizona
Maintain structural integrity of buildings

## Slide 15
Water leaks
Indicate faulty plumbing, damaged roofs, etc.
Attract mold, carpenter ants, termites, flies, and rodents
Weaken structures and lead to other problems
Repair water leaks promptly – Dawn H. Gouge, University of Arizona
Routine, Proactive Maintenance
Drywall water damage
- Herbert Bernstein, WikiMedia Commons

## Slide 16
Routine, Proactive Maintenance
Structural pests attracted to water damaged wood include: termites, wood-destroying beetles, and mold
Monitor for pest activity
Maintain structural integrity of buildings
Sign of western drywood termite damage - Kevin (ibkev2002), Flickr
Subterranean termite shelter tubes in a basement
- Larry Ralph Jr., Indiancrawlspacerepair

## Slide 17
Routine, Proactive Maintenance
Seal your buildings
Vertical and horizontal gaps
Avoid propping doors open
  Door sweeps can cut pest complaints by 65%
Prevent pest entry
Even if this door is not propped open, the vertical gap gives easy entry to flying and crawling pests – Dawn H. Gouge, University of Arizona

## Slide 18
Routine, Proactive Maintenance
Check escutcheon plates (pipe collars)
Seal around pipe-chases and conduits
Loose escutcheon plates – Dawn H. Gouge, University of Arizona
Prevent pest entry
Gap in drop ceiling - Janet Hurley, Texas AgriLife Extension

## Slide 19
Routine, Proactive Maintenance
Sealing gaps
Use high quality silicon based (elastomeric) sealants
Sealing gaps around window frames keeps pests out and reduces heating/cooling expenses -WikiMedia Commons
Gaps in wall at pipe entry points Gaps have been sealed
- J. G. Kaufmann, WikiMedia Commons

## Slide 20
Routine, Proactive Maintenance
Seal around windows, doors, gaps, wall penetrations
Eliminate unscreened access
Ensure air doors are set
Create space around your buildings
Prevent pest entry
Ensure that access panels are not left open – Jerry Jochim, Monroe County Community School Corporation
Ensure space between vegetation and building – Dawn H. Gouge, University of Arizona

## Slide 21
4.
Prune away from buildings
Tree limbs pruned at least six feet away
Remove vines climbing on buildings
Remove groundcover next to buildings
Routine, Proactive Maintenance
These shrubs need trimming and pruning – Dawn H. Gouge, University of Arizona

## Slide 22
Routine, Proactive Maintenance
Grate and drain covers should be removed and cleaned out periodically – Dawn H. Gouge, University of Arizona
Avoid pest conducive conditions
Clean debris out of external drainage catch areas
Prevent debris and moisture from accumulating near building walls and foundations
Pests such as rodents and flies are attracted to moist organic matter – Marc Lame, Indiana University

## Slide 23
Routine, Proactive Maintenance
Avoid pest conducive conditions
Pests such as cockroaches spend daytime hours harboring in cracks and crevices
Reduce harborage sites, especially in areas with food
Sealing around escutcheon plates – Jerry Jochim, Monroe County Community School Corporation

## Slide 24
A pesticide applicator license may be required for applicators on school property
Consider local, state, and federal laws
Be aware of allowable products and proper notifications
When Using Pesticides
Routine, Proactive Maintenance

## Slide 25: Timely Work Order Follow-Up
Enforce timely responses to pest problems related to building repairs
A small fix can avoid a big problem
Repeated reporting is a waste of staff time
Centralize reports and track resolution times and costs
Use work-order systems
Ensure doors close completely to keep pests out – Dawn H. Gouge, University of Arizona

## Slide 26
Sanitation and exclusion are basic steps in IPM
Sanitation involves cleaning, including the removal of hazardous wastes
Proper disposal of garbage and other wastes
Key Elements of Sanitation and Exclusion
Joseph Sohm, Shutterstock.com

## Slide 27
This dumpster is too close to the kitchen entryway
Good placement of dumpsters, in separate enclosed area, but lids should be closed
Waste management is an important part of sanitation
    Ensure dumpsters are:
      clean, covered, and well maintained
      placed on a concrete or asphalt surface
      placed 20-30 feet from building entryways
    Areas around the dumpster should be kept free of debris
Key Elements of Sanitation and Exclusion
Dawn H. Gouge, University of Arizona

## Slide 28: 1.
Your dumpster capacity should be sufficient
Emptied weekly
Monitor for resident dumpster pests
Poorly managed dumpsters and dumpster area – Marc Lame, Indiana University
Waste management
Key Elements of Sanitation and Exclusion
Notes: Objective 1

## Slide 29: 1.
Rotate out dirty dumpsters for clean ones
Dumpsters should be emptied at least weekly
Consider sealed, leak-proof, self-contained compactors, available in many sizes – Shaku Nair, University of Arizona
Waste management
Key Elements of Sanitation and Exclusion

## Slide 30
Proper storage of supplies and materials helps to:
prevent pest-conducive conditions
permit proper cleaning and inspection
Key Elements of Sanitation and Exclusion
Cardboard covered wooden pallets are pest prone
- Dawn H. Gouge, University of Arizona
Aluminum dunnage racks are ideal, as you can see and clean beneath them

## Slide 31
Cardboard boxes provide excellent pest harborage
Pest Exclusion Strategies/Tactics
Kitchen pantry, before and after cardboard removal (inspect, date and organize supplies as they arrive) - Marc Lame, Indiana University

## Slide 32
Equipment cleaning
Keep cleaning equipment in good and clean working condition
Hang brooms 6 inches off the vertical wall
Food can accumulate in:
  garbage receptacles
  brooms, dusters, and brushes
  mops and buckets
    vacuum cleaners, polishers, scrubbers
Natural fiber brooms are difficult to clean, select cleaning tools that are easy to maintain

## Slide 33: Cleaning Equipment Maintenance and Storage
Empty
Vacuum cleaners, floor scrubbers, and other equipment before storing
Wipe Down, Wash, and Rinse

## Slide 34: Cleaning Equipment Maintenance and Storage
Storage
Store items on off-the-floor racks, and away from the vertical wall
Store in transparent plastic totes or on wire shelving
Store equipment off the floor and in a manner that will allow it to dry rapidly – Dawn H. Gouge, University of Arizona

## Slide 35: Thorough cleaning procedures
Keep yourself safe, clean, and hygienic!
Wash hands

## Slide 36: Pest exclusion - denying pests access to food, water and shelter
Find a pest - search for points of entry
Door-sweeps and weather stripping
Hitchhikers in deliveries
Key Elements of Sanitation and Exclusion
This door needs new door-sweeps, vertical and horizontal – Dawn H. Gouge, University of Arizona

## Slide 37
Replace worn door-sweeps
Seal gaps, cracks, and crevices
Cover windows and vents with wire mesh
Pest Exclusion Strategies/Tactics
Torn wire mesh on a vent – Jerry Jochim, Monroe County Community School Corporation

## Slide 38
3.
P-traps in drains
Dry P-traps create access to buildings from the sewer
Inspect drains periodically to prevent P-traps from drying out
Pest Exclusion Strategies/Tactics

## Slide 39
Avoid propping doors
Close gaps
Avoid clutter, both inside and outside, especially near external doorways
This space needs de-cluttering!
This door should be closed
Pest Exclusion Strategies/Tactics
Jerry Jochim, Monroe County Community School Corporation

## Slide 40: 2.
What to look for:
Pests
Signs of pests
Pest conducive conditions
Key Elements of Inspection and Monitoring
Mouse poop on a spoon
Regular inspection and monitoring
Cockroaches feeding on crumbs
Dawn H. Gouge, University of Arizona

## Slide 41: 2.
Where to look:
Dark corners
Hard-to-reach areas
Undisturbed
Warm and/or wet places
Food storage and/or preparation areas
Waste collection containers/ areas
Suspended ceilings
Key Elements of Inspection and Monitoring
Regular, careful inspection helps to keep pests and pest-conducive conditions under control rapidly and efficiently – Dawn H. Gouge, University of Arizona

## Slide 42: 2.
Where to look:
Warm walls with penetrations
Compressor motor voids in equipment
Unsealed floors and floor to wall junctures
Undisturbed containers
Cardboard boxes
Clutter
Key Elements of Inspection and Monitoring
German cockroaches in telephone in heavily infested teachers lounge – Dawn H. Gouge, University of Arizona

## Slide 43
3.
Communicate in writing to IPM Coordinators and others about pest issues
Record date, time, location and:
If actual pests have been spotted
Signs (evidence) of pests
Pest-conducive conditions
Key Elements of Inspection and Monitoring

## Slide 44: 2.
Tools:
Monitoring traps
Bright flashlight
Hand lens
Key Elements of Inspection and Monitoring
Turkestan cockroaches on monitoring trap in teachers lounge – Dawn H. Gouge, University of Arizona

## Slide 45
Maintenance Staff and IPM
Clean and well-maintained school premises are essential for the health and well-being of all people who learn, play or work in the area – Dawn H. Gouge, University of Arizona

## Slide 46
Effective Communication
Maintenance staff know more about the school premises than most other staff
Get to know lead front-line staff, contractors, etc.
Communicate and educate your peers
Ricardo Zubiate teaching Salt Lake City School District Staff - Marc Lame, Indiana University

## Slide 47
Learn more about IPM
Ask questions
Discuss IPM and its advantages with your colleagues
Implementing IPM is easier with group support
Set an example
Effective Communication
Dr. Robert Corrigan, RMC Pest Management Consulting teaching - Mary Grisier, EPA Region 9

## Slide 48
“I am proud of
what I do to make my
school a better place
to learn and work”
Dan Vezie, Maricopa Unified School District, AZ
Maintenance Staff and IPM
Dan Vezie, Maricopa Unified School District receiving a recognition award – Shujuan Li, University of Arizona

## Slide 49: Check In!
In this lesson you learned:
The importance of routine, proactive maintenance to maintain structural integrity and prevent pest entry and pest conducive conditions
The importance of timely work order follow-up
Key elements of sanitation and exclusion, including: strategies, tactics and tools
Key elements of inspection and monitoring, including: what to look for, where to look, tools used and frequency
The importance of effective communication, education, and cooperation between school staff
  Congratulations, you have completed the School IPM for Maintenance Staff Module!

## Slide 50: Resources
Picture tour: IPM in Action – Safer Pest Control Project http://www.spcpweb.org/factsheets/IPM_Picture_Tour_w_cover.pdf
Get tough on pests in school facilities – NC State Cooperative Extension http://schoolipm.ncsu.edu/documents/Custodial_and_Maintenance_staff.pdf
School IPM for maintenance and grounds staff – IPM Institute http://schoolipm.ncsu.edu/documents/Custodial_and_Maintenance_staff.pdf
CA Dept. of Pesticide Regulation – IPM for Maintenance and Operations staff http://apps.cdpr.ca.gov/schoolipm/mo_staff/main.cfm
Implementing and IPM Program for Schools and Child care facilities – NC State University http://schoolipm.ncsu.edu/documents/Manual-Chapter2.pdf
Indoor and outdoor school IPM strategies http://www.extension.org/pages/20416/indoor-and-outdoor-school-ipm-strategies#.VNLCCy5kSpc